## Slide 1: EE 445L – Embedded System Design Lab
Instrumentation amp
For more information read Section 8.2.3 in the book

## Slide 2: Op amp review
Linear op amp circuit
  Maps a transducer to the ADC
  The five design rules
    Negative Feedback
    Rail-to-rail
    Vx ~= Vy
    Ix =0 and Iy = 0
    Select resistors in the 1kW – 1MW range
Parameters
  Linear equation: output as a function of input(s)
  Input impedance
  Output impedance
  Offset voltage
  Frequency response
  Noise compare it to signal resolution
EE 445L – Bard, Valvano

## Slide 3: OP AMP Example
(10) Exam Question 3. The output of a linear transducer is V1, and V1 is connected as the input to an amplifier. The amplifier has a transfer function of V2 = 100 (V1+0.02). The range of V1 is -0.02 to 0.02 V. V2 is connected as the input to an ADC. The ADC range is 0 to 4 V, and ADC precision is 10 bits. The sampling rate is 1000 Hz. What is the maximum allowable voltage noise of the amplifier, referred to its input? Show your work.

## Slide 4: Instrumentation Amplifiers
Necessary condition (must be)
  amplify a differential voltage
  shown below as V2-V1
Sufficient condition (one or more may be true)
  large gain (above 100),
  a high input impedance, and
  a good common mode rejection ratio. Or low noise
EE 445L – Bard, Valvano

## Slide 5: INA122 Amp
INA122 is low-power single supply rail-to-rail instrumentation amp,
  Vout = Gain*(V1-V2) + Vref
  (AD627 or INA122) Gain = 5+(200kΩ/RG)
  Vout = Vref when V1 equals V2
In Lab 9, ground pin 5 (Vref = 0)
  Vout = Gain *(V1 – V2)
EE 445L – Bard, McDermott, Valvano

## Slide 6: Shunt Diode Reference
LM4041CILPR
  Rs sets maximum current
  R1,R2 sets voltage
  Iz = 80uA + Vref /(R2+R1)
  Vd = 1.233V (across R1)
  Vref = Vd (1 + R2/R1)
  Max Iref = (3.3- Vref)/Rs - Iz
EE 445L – Bard, McDermott, Valvano

## Slide 7: EKG
Differential signal
2500 gain, good CMRR
Better (avoids saturation from CM)
Instrumentation amp gain is 10
Op amp gain is 200
EE 445L – Bard, McDermott, Valvano

## Slide 8: Resistance bridge
Differential signal
Large Zin
EE 445L – Bard, McDermott, Valvano

## Slide 9: Thermocouple Amp
Differential signal
Large Zin
Large gain
EE 445L – Bard, McDermott, Valvano
3.3V
3.3V

## Slide 10: Summary
Necessary condition
  Differential signal
  E.g., resistance bridge, biopotentials
Sufficient conditions
  High gain
  Large input impedance
  Good CMRR